## Slide 1: CUT TO LENGTH APPLICATION
FOR SHEET PROFILE MACHINE

## Slide 2: CONTENT
Customer
Machine specification and working
Product used
Application features

## Slide 3: 1. CUSTOMER
Smart Tech Automation, Navi Mumbai
End user: Ananta Engineering, Khopoli

## Slide 4: 2. Machine specification and working
MATERIAL:
Coil Width: 1000 mm~1250mm
Suitable Coil Thickness: 0.3mm - 0.6mm
Suitable Raw Materials: Pre-painted Coil
MACHINE COMPONENTS:
Un-coiler unit
Roll-Forming machine
PLC and drive control system
Hydraulic cutting system
Product rack (Optional)

## Slide 5: 2. Machine specification and working
WORKING:
Cutting as per set length
Using 1024PPR encoder calculates sheet length and once set length equals actual length cutter cuts sheet
Once set cut and actual number of cuts are equal machine stops
Manual jog for adjustment
Manual and auto Operations

## Slide 6: 3. Product used
Inovance
PLC & HMI :- H0U-0808MRT-6AT
  8 DI and 8 DO, 2 AI and 2 AO, 2 temperature detection input
Drive :- MD310T7.5B
  7.5kW drive
Others
Motors :- 7.5kW main motor and 3.7kW for un-coiler (Optional)
Encoder :- 1024 PPR
Proxy switches (2 nos.) for cutter unit (NPN type)

## Slide 7: 4. Application features
Length accuracy less than 1mm
Machine speed 12-15 mpm
Machine auto stop once set batch count is completed
Cutter operation
  When set length equals actual length and if cutter is enabled then shear will cut sheet otherwise wait for command
  When shear cuts, blade will stop until machine perform reverse jog for 5-15mm to avoid material damages
  Then blade will come to it’s home position and machine will start again
Two jog speeds selection from HMI

## Slide 8: THANK YOU